## Slide 1: Digital Signal Processing
Abu saleh Musa Miah
Lecturer, Dept. of CSE, BAUST, Bangladesh email: musa@baust.edu.bd, tel: +88-01727-786600 web: www.baust.edu.bd/cse

## Slide 2
www.tutorialcare.com/DSP
Textbook：
Digital signal processing - Principles, algorithms and application (3nd Edition)
J G Proakis, D G Manolakis
Reference for experiment：
Slicer_Digital_Signal_Processing_Using_MATLAB_
3rd_Edition
Textbook for Shortcut Understanding：
Understanding Digital Signal Processing
Richard G.Lyons
Digital Signal Processing

## Slide 3: What is DSP?
DSP’s process signals
Converting a continuously changing waveform (analog) into a series of discrete levels (digital)

## Slide 4: What is digital signal processing (DSP)?
Digital Signal Processing is a field of numerical mathematics that is concerned with the processing of discrete signals
This area of mathematics deals with the principles that underlie all digital systems

## Slide 5: Typical System Components

## Slide 6: Application Areas of DSP:
  EEG signal process
      Enhancement-noise filtering
      Coding, synthesis, and recognition
      Classification
  Speech signal processing,
      Enhancement-noise filtering
      Coding, synthesis, and recognition
      Classification
  Sonar and radar signal processing, ,
  Digital image processing,
  Signal processing for communications,
  Control of systems,
  Biomedical signal processing,
  Seismic data processing, etc.

## Slide 7: Applications of DSP: Biological signal
Examples:
  Brain signals (EEG)
  Cardiac signals (ECG)
  Medical images (x-ray, PET, MRI)
Goals:
  Detect abnormal activity (heart attack)
  Help physicians with diagnosis
Tools: Filtering, Fourier Transform

## Slide 8: Applications of DSP: Biometrics
Identifying a person using physiological characteristics
Examples:
  Fingerprint Identification
  Face Recognition
  Voice Recognition

## Slide 9: What is Signal?
A flow Information
A detectable physical quantity or impulse (as a voltage, current, or magnetic field strength) by which messages or information can be transmitted (Webster Dictionary)
Varies with time, space or any other independent variable or variables.

## Slide 10: What is Signal?
A system is defined as a physical device that perform an operation on a signal.
Example: A filter used to reduce noise.
Systems respond to signals and produce new signals
Excitation signals are applied at system inputs and response signals are produced at system outputs

## Slide 11: System
the system is characterized by the type of operation that it performs on the signal.
If the operation is linear, the system is called linear. If the operation on the signal is nonlinear, the system is said to be nonlinear, and so forth.
Such operations are usually referred to as signal processing.

## Slide 12: Signal
Signal Characteristics:
  Signals are Physical Quantities:
  Signals are Measurable
  Signals are Analog
  Signals Contain Information.
Examples:
  Temperature [oC]
  Pressure [Newtons/m2] or [Pa]
  Mass [kg]
  Speed [m/s]
  Acceleration [m/s2]
  Torque [Newton*m]
  Voltage [Volts]
  Current [Amps]
  Power [Watts]
In this class, analog signals are electrical.
  Sensors: are devices that convert other physical quantities (temperature, pressure, etc.) to electrical signals.

## Slide 13: Example of Signal
Figure1: DC Signal.
The output voltage vout is defined by the following equation:
  Simple form of signal is DC (Direct Current) signal as in Figure 1.

## Slide 14: Example of Signal
if vs=5, we can write the signal as x(t)=5 is a very simple form of signal.
Another form of signal is AC (Alternating Current) signal as in figure 2.
Figure 2: A continuous time signal x(t).

## Slide 15: Example of Signal
Human vocal mechanism produces speech. Where acoustic pressure is as a function of time t. We can convert this into electrical signal using microphone and this is called speech signal. This signal is complex and can not be represented easily. Figure 3 shows speech signal.
Figure 3: speech signal or acoustic signal.
In Image signal, where a picture can be represented by brightness as a function of two spatial variables f(x,y) as in figure 4.

## Slide 16: Example of Signal
Figure 4: Picture elements and coordinate to represent digital image.

## Slide 17: Signal (Example)

## Slide 18: Independent Variable
Time is often the independent variable for a signal. x(t) will be used to represent a signal that is a function of time, t.
A temporal signal is defined by the relationship of its amplitude (the dependent variable) to time (the independent variable).
An independent variable can be 1D (time), 2D (space), 3D (space) or even something more complicated.
The signal is described as a function of this variable.
There are many types of functions that can be used to describe signals (continuous, discrete, random).

## Slide 19: Signal
(1.1.1)
describe two signals. one that varies linearly with the independent variable r (time)
and a second that varies quadratic ally with t .
As another example, consider the function
S(x,y)=3x+2xy+10 (1.1.2)

## Slide 20: Signal
The signals described by (2.1.1) and (1.1.2) are class of signals defined functional dependence on independent variable.
However, there are cases functional relationship is unknown or highly complicated in practical use.
For example, a speech signal (see Fig. 1.1) cannot be described functionally by expressions such as (1.1.1).
In general, a segment of speech represented to a high degree of accuracy as a sum of several sinusoids of different amplitudes and frequencies, that is, as

## Slide 21: Signal
where are the sets of (possibly time-varying) amplitudes, frequencies, and phases, respectively, of the sinusoids.
In fact, one way to interpret the information content or message conveyed by any short time segment of the activity of the brain.

## Slide 22: Signal
Speech, electrocardiogram(ECG) and electroencephalogram (EEG) signals are single independent variable. namely time.
Two independent variables is an image signal.
Speech signals are generated by forcing air through the vocal cords.
Vocal cords and the vocal tract, also called the vocal cavity.
Images are obtained from photographic film to a scene.
Signal generation is usually associated with a system that responds to a stimulus or force.
The stimulus in combination with the system is called a signal source.

## Slide 23: Analog or continuous Time Signal
Most of the signals in the physical world are CT signals, since the time scale is infinitesimally fine (e.g., voltage, pressure, temperature, velocity).
Often, the only way we can view these signals is through a transducer, a device that converts a CT signal to an electrical signal.
Common transducers are the ears, the eyes, the nose… but these are a little complicated.
Simpler transducers are voltmeters, microphones, and pressure sensors.

## Slide 24: Analog Signal
Amplitude
Phase
Frequency
x(t) = 5 cos (2.pi.f.t)
x(t) = 5 cos (2.pi.f.t + 3.14)
x(t) = 5 cos (3. 2.pi.f.t + 3.14)

## Slide 25: Signal in Time Domain
Stationary signal
Frequency content of stationary signals do not change in time.
All frequency components exist at all times

## Slide 26: Signal in Time Domain
Non-Stationary signal
Frequency content of stationary signals change in time.
Magnitude
20 Hz
80 Hz
120 Hz

## Slide 27: Signal in Time Domain
Speech and noise signal
Noise is the unwanted signal that interfere
Speech is the message content or information conveyed
Speech
Broad band (100-10000Hz)
Non-stationary
Noise
Unknown
Slowly varying (fan) or
non-stationary (babble)
wideband or narrow band

## Slide 28: Signal in Time Domain
ECG
EEG
EMG
Almost all biological signals are non-stationary. Some of the most famous ones are ECG (electrical activity of the heart, electrocardiograph), EEG (electrical activity of the brain, electroencephalogram), and EMG (electrical activity of the muscles, electromyogram).

## Slide 29: Why signals should be processed?
Signals are carriers of information
Useful and unwanted
  Extracting, enhancing, storing and transmitting the useful information
  Amplitude
  Phase
  Frequency
  Spectral Content
How signals are being processed?---
  Analog Signal Processing vs.
  Digital Signal Processing

## Slide 30: Comparison of DSP over ASP
-Advantages
Developed Using Software on Computer;
Working Extremely Stable;
Easily Modified in Real Time ;
Low Cost and Portable;
-Disdvantages
Lower Speed and Lower Frequency

## Slide 31: Concept Frequency in CT and Discrete signal
From physics we know that frequency is closely related to a specific type of periodic motion called harmonic oscillation.
which is described by sinusoidal functions.
Periodicity
Recall if a signal x(t) is periodic, then there exists a T>0 such that x(t) =x(t+T) If no T>0 can be found, then x(t) is non-periodic.

## Slide 32: Continuous-Time Sinusoidal Signals
A simple harmonic oscillation is mathematically :
x ( t ) denotes an analog signal.
A is the amplitude of the sinusoid.
is the frequency in radians per second (radis), and
is the phase in radians.
Instead of Omega, we often use the frequency F in cycles per second or hertz (Hz).

## Slide 33: Continuous-Time Sinusoidal Signals
Figure 1.10 Example of an analog sinusoidal signal.

## Slide 34: Properties of C Sinusoidal Signals
Al. For every fixed value of the frequency F, is periodic. Indeed. it can easily be shown, using elementary trigonometry, that
where T, = 1/F is the fundamental period of the sinusoidal signal.
A2. Continuous-time sinusoidal signals with distinct (different) frequencies are themselves distinct.
A3. Increasing the frequency F results in an increase in the rate of oscillation of the signal, in the sense that more periods are included in a given time interval.

## Slide 35: Properties of C Sinusoidal Signals

## Slide 36: Discrete time Sinusoidal Signals
A discrete-time sinusoidal signal may be expressed as
A is the amplitude of the sinusoid.
w is the frequency in radians per sample. and is the phase in radians.
If instead of we use the frequency variable defined by
We can rewrite the equation:
Figure 1.12 shows a sinusoid with frequency w = /6 radians per sample (f = & cycles per sample) and phase 6 = 17/3.

## Slide 37: Discrete time Sinusoidal Signals

## Slide 38: Properties of Discrete time Sinusoidal Signals
B1. A discrete-time sinusoid is periodic only if its frequent?. f is a rational number. When
Proof:

## Slide 39: Properties of Discrete time Sinusoidal Signals
B2. Discrete-time sinusoids whose frequencies are separated by an integer multiple of are identical.

## Slide 40: Properties of Discrete time Sinusoidal Signals
B3. The highest rate of oscillation in a discrete-time sinusoid is attained

## Slide 41: Properties of Discrete time Sinusoidal Signals

## Slide 42: Analog to Digital Recording Chain
ADC
Continuously varying electrical energy is an analog of the sound pressure wave.
Microphone converts acoustic to electrical energy. It’s a transducer.
ADC (Analog to Digital Converter) converts analog to digital electrical signal.
Digital signal transmits binary numbers.
DAC (Digital to Analog Converter) converts digital signal in computer to analog for your headphones.

## Slide 43: DSP System

## Slide 44: A/D conversion

## Slide 45: Example of ADC

## Slide 46: Analog to Digital (A/D) Conversion
To process analog signals by digital means,
First necessary to convert them into digital form, that is, to convert them to a sequence of numbers having finite precision.
This process is called analog-to digital (A/D) conversion.
A/D conversion has Three steps
  Sampling
  Quantization
  Coding

## Slide 47: 1-Sampling
Conversion of a continuous-time signal into a discrete-time signal. It is called samples. Thus if xa(t) is the input to the sampler, the output is xa (nt) = x(n), where T is the sampling interval.
Here t is the sampling interval generally sampling rate is at least double of the frequency.

## Slide 48: 2-Quantization
Quantization is the process of converting the sampled analog voltages into digital words.
converting a continuous range of values into a finite range of discrete values.
We denote the quantization operation on the samples x(n) as Q[x(n)] and let xq(n) denote the sequence of quantized samples at the output of the quantizer. Hence
xq(n)= Q[x(n)]
Error, eq(n)= xq(n)-x(n)
3.Coding:
It is assigned a unique binary number to each quantized level. If we
have L levels we need at least L different binary numbers.
If L= 4, then binary bits b, is
The difference between unquantize sample x(n) and quantized sample is called quantization error

## Slide 49: Sampling
Sampling is a continuous to discrete-time conversion
Most common sampling is periodic
T is the sampling period in second
fs = 1/T is the sampling frequency in Hz
Sampling frequency in radian-per-second s=2fs rad/sec
Use [.] for discrete-time and (.) for continuous time signals
This is the ideal case not the practical but close enough
  In practice it is implement with an analog-to-digital converters
  We get digital signals that are quantized in amplitude and time
-3
-2
2
3
4
-1
1
0

## Slide 50: Periodic Sampling
Sampling is, in general, not reversible
Given a sampled signal one could fit infinite continuous signals through the samples
0
-1
20
40
60
80
100
-0.5
0
0.5
1
Fundamental issue in digital signal processing
  If we loose information during sampling we cannot recover it
Under certain conditions an analog signal can be sampled without loss so that it can be reconstructed perfectly

## Slide 51: ADC: Step1: Sampling Analog Signal
Process of recording analog signal into discrete time.
Sampling rate is number of samples per second.
Where is the discrete time signal obtained by “ taking sample of the analog signal every T second.
Sampling Rate:
The time interval between samples is called the sampling interval
(1.4.2)
(1.4.1)
There exists a relationship between the frequency variable F for analog signals and the frequency variable f for discrete-time signals.

## Slide 52: Sampling

## Slide 53: Relationship between the frequency of analog signal and the frequency of discrete-time signal
To establish relationship consider an analog signal
when, sampled periodically at a rate of samples per second
So (i) could be written as
…..(ii)
Comparing (ii) with x
the general equation of discrete time sinusoidal signals we find ,
f=FT
f = ………(iii) [relation]

## Slide 54: Relationship between the frequency of analog signal and the frequency of discrete-time signal
f=FT
f = ………(iii) [relation]
discrete time sinusoidal signals ,
- ………(iv)
Now substituting from (iii) into (iv)
Thus we find that the frequency F of continuous time sinusoidal signals when sampled at a rate of must fall in the above range.
We also can find that if the max frequency of discrete time sinusoidal is f then with a sampling rate

## Slide 55: ADC: Step1: Sampling Analog Signal
Since the highest frequency in a discrete-time signal is or .
It with a sampling rate ,
The corresponding highest values of F

## Slide 56: Sampling
Collect sufficient data for correctly representing a
continuous-time signal

## Slide 57: Difference between Continuous and Discrete time signal

## Slide 58: Analog to Digital Overview
[ “sample word length,” “bit depth”] Precision of numbers used for measurement: the more bits, the higher the resolution.
Example: 16 bit
Sampling Rate
How often analog signal is measured
Sampling Resolution
[samples per second, Hz]

## Slide 59: Sampling Rate/Sampling Theorem
Sampling/Nyquist Theorem:
Sampling rate must be at least twice as high as the highest frequency you want to represent.
Determines the highest frequency that you can represent with a digital signal.
If the highest frequency contained in an analog signal xa(t) is Fmax. And the signal is sampled at a rate Fs >= 2Fmax, then xa(t) can be exactly recovered from its sample values.
The sampling rate, FS >=2Fmax is called the Nyquist rate.

## Slide 60: Recovery of a sampled sine wave for different sampling rates

## Slide 61: Aliasing: signal ambiguity in FD
What happens if sampling rate not high enough?
A high frequency signal
sampled at too low a rate
looks like …
… a lower frequency signal.
That’s called aliasing or foldover. An ADC has a low-pass anti-aliasing filter to prevent this.
Synthesis software can cause aliasing.

## Slide 62: Anti-Aliasing Filter
An anti-aliasing filter removes frequencies that are higher than half the sampling rate using what is called a low pass filter. A low pass filter lets the low frequencies “pass" and "cut" the high frequencies. Low pass filters are sometimes called high cut filters.

## Slide 63: Common Sampling Rates
Sampling Rate | Uses
44.1 kHz (44100) | CD, DAT
48 kHz (48000) | DAT, DV, DVD-Video
96 kHz (96000) | DVD-Audio
22.05 kHz (22050) | Old samplers
Most software can handle all these rates.
Which rates can represent the range of frequencies audible by (fresh) ears?

## Slide 64: Step2 Quantization
Process of converting the sampled continuous-Valued signals into discrete-valued data

## Slide 65: Explain quantization of continuous –amplitude signal
Converting a discrete time continuous amplitude signal into a digital signal called quantization.
The quantized value x(n) is
Here the quantization error is a sequence
Difference between the quantized value and actual sample value.
, the instantaneous quantization error can not exceed half of the quantization step.
Quantization converts the samples in values those are in a finite set.

## Slide 66: Explain quantization of continuous –amplitude signal
The values allowed in the digital signal called quantization levels.
Distance between two successive quantization levelsis called quantization step size or resolution .
The rounding quantizer assigns each sample of x(n) to the nearest quantization levels .
Qruncation quantizer assigns each sample of x(n) to the quantization level below to it.

## Slide 67: A/D: Step2: Quantization
Amplitude values ranging between two limits: a min and a max.
Amplitude values are infinite between the two limits.
We need to map the infinite amplitude values onto a finite set of known values.
This is achieved by dividing the distance between min and max into L zones, each of height 
 = (max - min)/L

## Slide 68: Explain quantization of continuous –amplitude signal
If represent the maximum and minimum value of x(n) and L is the number of quantization levels then
is called the dynamic range of the signal.
L is also obtained from here the quantization has b bits of accuracy.
If the dynamic range of the signal is fixed ,increasing the number of quantization levels we can increase the accuracy of the quantization and decrease the step size.

## Slide 69: Assigning Codes to Zones
Each zone is then assigned a binary code.
The number of bits required to encode the zones, or the number of bits per sample as it is commonly referred to, is obtained as follows:
nb = log2 L
Given our example, nb = 3
The 8 zone (or level) codes are therefore: 000, 001, 010, 011, 100, 101, 110, and 111

## Slide 70: 3-bit Quantization
0
1
2
3
4
5
6
7
Amplitude
Time — measure amp. at each tick of sample clock
A 3-bit binary (base 2) number has 23 = 8 values.

## Slide 71: 4-bit Quantization
A 4-bit binary number has 24 = 16 values.
0
2
4
6
8
10
12
14
Amplitude
A better approximation
Time — measure amp. at each tick of sample clock

## Slide 72: Quantization Error
When a signal is quantized, we introduce an error - the coded signal is an approximation of the actual amplitude value.
The difference between actual and coded value (midpoint) is referred to as the quantization error.
The more zones, the smaller  which results in smaller errors.
BUT, the more zones the more bits required to encode the samples -> higher bit rate

## Slide 73: Quantization Noise
Round-off error: difference between actual signal and quantization to integer values…
Random errors: sounds like low-amplitude noise

## Slide 74
Consider an audio signal with a voltage range between -10 and +10
Assume the audio waveform has already been time sampled, as shown
How can the amplitude also be converted into discrete values?

## Slide 75
For this example, let’s choose to represent each sample by 4 bits
There are an infinite number of voltages between -10 and 10.
We will have to assign a range of voltages to each 4-bit codeword.
There will be 16 steps. Why?
How large will each step be?

## Slide 76: QUANTIZATION

## Slide 77: A/D: step3: Coding
Data coding
Data coding separates the digital words so that they are more easily identified.

## Slide 78: Digital to Analog Conversion: Sample and Hold
To reconstruct analog signal, hold each sample value for one clock tick; convert it to steady voltage.
0
1
2
3
4
5
6
7
Amplitude
Time

## Slide 79: DAC: Smoothing Filter
Apply an analog low-pass filter to the output of the sample-and-hold unit: averages “stair steps” into a smooth curve.
0
1
2
3
4
5
6
7
Amplitude
Time