## Slide 1: Digital Signal Processing LTI System
Abu saleh Musa Miah
Lecturer, Dept. of CSE, BAUST, Bangladesh email: musa@baust.edu.bd, tel: +88-01727-786600 web: www.baust.edu.bd/cse

## Slide 2: Define LTI system?
The digital signal processing is concerned exclusively with a particular class of system known as linear time invariant system.
In LTI systems the output is the convolution between the input signal and system impulse response.
convolution is a mathematical operator which takes two functions f and g and produces a third function that in a sense represents the amount of overlap between f and a reversed and translated version of g.
to set as input to any LTI system any arbitrary signal is need to be decomposed and represented as in weighted sum of unit sample sequences.
We will learn that multiplication in frequency domaing is equivalent of convolution in time domain

## Slide 3: Define LTI system?
Making a system with Combination of Linearity and time invariant property of a signal.
We know any sequence we can write
-(1)
It follows that a linear system can be completely characterized by its impulse response.
Let is the response of a system to the input , an impulse occurring at n =k,
Using the eq(1) to represent the input, it follows that
If only linearity is imposed then depend both n and k
…(2)

## Slide 4: Define convolution sum?
Property of time invariance implies that if h[n] is the response to then the response to is h. With this addition constraint we can rewrite that.
for all n. –(3)
where y[n] is the output obtained by passing an input signal x[n] through a filter whose coefficients are h[n].
Here, the limits of summation range from 0 to N as our h[n] signal is finite in nature.
this called convolution sum, and we represent this by the operator notation
y(n)=x(n)*h(n). where * denotes the convolution operation.

## Slide 6: Convolution Sum

## Slide 7: LTI
Our first observation is that the index in the summation is k, and hence both the input signal x(k) and the impulse response h(no - k ) are functions of k.
Second, we observe that the sequences x(k) and h(no - k) are multiplied together to form a product sequence. The output y(na) is simply the sum over all values of the product sequence.
The sequence h(no - k) is obtained from h(k) by, first, folding h(k) about k = 0 (the time origin), which results in the sequence h(- k). The folded sequence is then shifted by no to yieid h(no - k ) .
To summarize, the process of computing the convolution between x ( k ) and h(k) involves the following four steps.

## Slide 8: Three different process of computing convolution sum?
Mathematical approach
Tabular approach
Graphical approach

## Slide 9: Mathmatical Aproach
Let length of sequence x(n) is N1,
lower limit of x(n) is n1,upper limit of x(n) is n2.
length of sequence h(n) is N2,
lower limit of x(n) is p1, upper limit of x(n) is p2.
(a)Let length of sequence y(n) is :-
length of sequence x(n) is
+ length of sequence h(n) is -1
n=N1+N2-1
(b) lower limit of y(n) is :-
lower limit of x(n) is + lower limit of h(n) is
y(n)=n1+p1
(c) upper limit of y(n) is :-
upper limit of x(n) is + upper limit of h(n) is
y(n)=n2+p2

## Slide 10: Mathmatical Aproach
now for the mathematical approach ,
And this n will vary from n1+p1 to n2+p2
n1+p1 n2+p2

## Slide 11: Mathmatical Aproach
Try to understand upper limit and lower limit

## Slide 12: the input sequence x(n)={3^,1,2,-1} sequence is applied to discrete time processor with unit sample response h(n)={3^,2,1}
Length of y(n)=4+3-1 =6
Lower limit of y(n)= 0+0=0 ,
Upper limit of y(n)=3+2 =5
n=0,
=x(0)h(0) + x(1)h(-1) + x(2)h(-2) + x(3)h(-3)
=3.3+1.0+2.0+(-1).0 =9
n=1,
=x(0)h(1) + x(1)h(0) + x(2)h(-1) + x(3)h(-2)
=3.2+1.3+2.0+(-1).0 =9

## Slide 13: the input sequence x(n)={3^,1,2,-1} sequence is applied to discrete time processor with unit sample response h(n)={3^,2,1}
n=2,
=x(0)h(2) + x(1)h(1) + x(2)h(0) + x(3)h(-1)
=3.1+1.2+2.3+(-1).0
=11
n=3,
=x(0)h(3) + x(1)h(2) + x(2)h(1) + x(3)h(0)
=3.0+1.1+2.2+(-1).3
=2

## Slide 14: the input sequence x(n)={3^,1,2,-1} sequence is applied to discrete time processor with unit sample response h(n)={3^,2,1}
n=4,
=x(0)h(4) + x(1)h(3) + x(2)h(2) + x(3)h(1)
=3.0+1.0+2.1+(-1).2
=0
n=5,
=x(0)h(5) + x(1)h(4) + x(2)h(3) + x(3)h(3)
=3.0+1.0+2.0+(-1).1
= -1
Thus , y(n) = {9^,9,11,2,0,-1}

## Slide 15: Tabular approach:-
Consider a table N1 N2
For the above example 4
Now summations of all element in each partition is the value of members of y(n).
Like x(0)h(0) is in 0th partition so it is the value of y(n) . x(0)h(1)+ x(1)h(0) is in the 1st partition so it’s the value of y(n)
 | h(0) | h(1) | h(2)
x(0) | x(0)h(0) | x(0)h(1) | x(0)h(2)
x(1) | x(1)h(0) | x(1)h(1) | x(1)h(2)
x(2) | x(2)h(0) | x(2)h(1) | x(2)h(2)
x(3) | x(3)h(0) | x(3)h(1) | x(3)h(2)

## Slide 16: Graphical Approach

## Slide 17: Graphical Approach
Similarly we can find y(3)=3 ,y(4)= -2 , y(5) =- 1,as the upper bound is 2+3 = 5 so we will stop here. and as the lower bound is 0+(-1) = -1 we have to find y (-1).
For that we have to shift h(-k) to left by 1 position to get h(-1-k)

## Slide 18: Graphical Approach
only 0th and 1st ,2nd ,3rd positions in both sequences holds non zero values so the product will have value in only those placed .
now y(2)= sum of all terms in (2) = -1+2+6+1 = 8

## Slide 19: process of computing convolution sum?
The processes of computing convolution between x(k) and h(k) involves the following steps
folding:- fold h(k) about k=0 to get h(-k)
shifting :- shift h(-k) by n0 right if n0 is positive or left otherwise to obtain .h(n0-k).
Multiplication :-multiply x(k) by h(n0-k) to obtain the product sequence
Summation :- sum all the values of product sequence to obtain the value of the response at time n=n0.

## Slide 20: Example:

## Slide 21: Example:

## Slide 22: Example:

## Slide 23: Example:

## Slide 24: Example:

## Slide 25: Example:
Consider the input x[n] = {2, 3, 4} of a LTI system and impulse response h[n] = {2, 1}. Find out the convolution sum of output y[n] of the LTI system.
Solution:
Given,
The input of the LTI system, x[n] = {2, 3, 4}
The impulse response h[n] = {2, 1}.
Form the convolution sum theorem, the order of the index of impulse response will de changed as h[-n] = {1, 2}.

## Slide 26
Now the convolution sum output will be computed using the equation
Now, we compute, y(0), y(1), y(2), y(3), y(4), ......

## Slide 32: Figure: Output, y(n):

## Slide 33: Properties of the convolution sum:

## Slide 34: properties of convolution sum?
Commutative :-
The convolution operation is Commutative,
x(n)*h(n)= h(n)*x(n)
proof:
from the definition of convolution ,
let ( n- k)=p , now as
.
= h(n)*x(n)
Hence it is cumulative.

## Slide 35: properties of convolution sum?
Distributive with respect to addition :-
The convolution operation is distributive with respect to addition ,
x(n)
proof:
from the definition of convolution
x(n)
Thus , The convolution operation is distributive with respect to addition.

## Slide 36: properties of convolution sum?
Associative :-
The convolution operation is associative,
Proof :
Since convolution is commutative
y(n-k)*h(n-k)= h(n-k)*y(n-k)
hence ,

## Slide 37: properties of convolution sum?
hence ,
=>h(n)*[x(n)*y(n)] =[x(n)*y(n)]*h(n)
Thus convolution is associative

## Slide 38: Discuss the connection of LTI System
Cascade system: -
In this types of connection output of (n-1)th system is connected to the input of the nth system. Let z(n) is the output of the first system and y(n) is the output of the second system and h(n) is the response of the entire system
here z(n) = x(n)*(n)
y(n)= z(n)*
= [x(n)*(n) ]*
= x(n)*[(n) * ]
Hence the response of the entire system is given by ,
[(n) * ]

## Slide 39: Discuss the connection of LTI System
Parallel system:-
In this types of connections each system produces individual output .and finally the are added and the output of entire system is generated.
Step 6:- shift to right h(1-k) by 1 to get h(2-k)
only 0th positions in both sequences holds non zero values so the product will have value in only 0th placed .
now y(-1)= sum of all terms in (-1) = 1

## Slide 40: Discuss the connection of LTI System
Parallel system:-
If
Then we get y(n) as below,
y(n)=
Hence the output y(n) is given by
And the response of the system as

## Slide 41: Types of LTI System ?
Casual anti-causal
The output of a causal system depends at most on current or past inputs like x(n),x(n-1),x(n-2)……..
But never on future inputs.
The output of a LTI system is given by convolution of x(n) and h(n) [unit sample response ],
y(n)=x(n)*h(n)
+

## Slide 42: Types of LTI System ?
Casual anti-causal
Here n+2 , n+2 …are the future inputs so for the causality properties h(-1) = h(-2) =…….=0
Means h(n) =0 ,when n< 0
Hence for LTI system causality condition is given by
output of a causal discrete LTI system
output of an anti-causal discrete LTI system

## Slide 43: Types of LTI System ?
Stable unstable
For a bounded set input is a system generates a bounded output then it is called stable system and unstable otherwise
Output of LTI system is given by,
y(n)=x(n)*h(n)
If the input sequence is bounded then the necessity condition for stability is

## Slide 44: Types of LTI System ?
Static dynamic
If the output of any system only depends on the current inputs and no storage is needed then the system is called static and dynamic otherwise.
is a static system.
FIR and IIR
Depending on the impulse response sequence the system is divided into two classes ,if the impulse response sequence is of finite duration then the system is called FIR, If h(n) is non-zero for n=0 to n- N-1, then the equation for FIR system is given by
if the impulse response sequence is of infinite duration then the system is called IIR,
If h(n) is non-zero for n>0 , then the equation for IIR system is given by

## Slide 45: Types of LTI System ?
Recursive non recursive
There are some system which not only requires the past and current inputs to generate desired output, but also it needs the already available past outputs .
Consider a system tries to calculate cumulative average of x(n) in the interval
Defined as ,
To compute this the system needs to store all the input samples, and with the increase of n the storage requirement increases in time.
This could be simplified as storing some past outputs like y(n-1)

## Slide 46: Types of LTI System ?
Recursive non recursive
In general , a system who’s output y(n) at time n depends on any number of past output values y(n-1), y(n-2),…………is called a recursive system
The general difference equation of LTI system?
The zero state response or relaxed response of a recursive system is given by ,

## Slide 47: Types of LTI System ?
The general difference equation for LTI system is expressed as,
,
y(n)
Norder of the system
Now N=1,M=0,,
And y(n)=ay(n-1) +x(n)
=
+
Now

## Slide 48: Types of LTI System ?
The general difference equation for LTI system is expressed as,
Now
Consider,
y(n)= -x(n)
y(0)= -x(0)
y(1)= -x(1)
= -x(0) } + x(1)
= (- y(-1) + (- x(0) +x(1)
Y(2) = (- y(-1)+ (- x(0) +(- x(1) + x(2)

## Slide 49: Correlation
Correlation addresses the question: “to what degree is signal A similar to signal B.”
An intuitive answer can be developed by comparing deterministic signals with stochastic signals.
  Deterministic = a predictable signal equivalent to that produced by a mathematical function
  Stochastic = an unpredictable signal equivalent to that produced by a random process

## Slide 50: Correlation
Correlation is maximum when
  Two signals are similar in shape
  And are in phase (or unshifted)
Correlation is measure of similarity between two signals as a function of time shift between them

## Slide 51: Correlation
Correlation functions shows how similar two signals are, and how long they remain similar when one is shifted with respect to the other

## Slide 52: Autocorrelation
  Correlating a signal with itself

## Slide 53: Xcorrelation to identify a signal
Cross-correlation of x(n) and y(n) is a sequence, rxy(l)

## Slide 54
Thanks for your attention